## Slide 1: Annual Conducted Electrical Weapon (CEW) User Update
Version 20.2
Effective: January 15, 2018
Notes: This PowerPoint® presentation is intended to assist law enforcement agencies in providing annual recertification training to their law enforcement officers. It does not replace any Conducted Electrical Weapon (CEW) Training Program, and is not intended for initial end-user certification.
All TASER® Training Materials are copyrighted and:
  Must be used in their entirety (PowerPoint slides, video, and instructor notes)
  May only be used by TASER certified instructors holding a current certification on the CEW model being taught
  May not be used for commercial purpose
  If you use TASER Training Materials, you accept and agree to be bound by Axon Enterprise, Inc.’s License Agreement.
Nothing in this PowerPoint, TASER CEW Smart Use Considerations, or associated materials establishes any standard of care. These guidelines may be more conservative than Constitutional standards.
Each law enforcement agency is solely responsible for its training programs and use-of-force policies. Always review and incorporate your agency’s policies, procedures, general orders, and relevant case law into your CEW training.
Axon does not give legal advice and nothing contained herein creates any form of attorney-client relationship. Consult your personal, local, law enforcement agency, or governmental advisor for any legal advice or guidance.
As required by TASER instructor training, you must check the Axon website within 72 hours of using this presentation to ensure use of the most current warnings and training materials. https://www.axon.com/training/resources
Axon, X2, X26, X26P, M26, TASER, Smart Cartridge, SPPM, and the “Bolt within Circle Logo” are trademarks of Axon Enterprise, Inc., some of which are registered in the US and other countries. For more information, visit www.axon.com/legal. All rights reserved. © 2018 Axon Enterprise, Inc.
© 2018 Axon Enterprise, Inc.

## Slide 2: ANNUAL CEW USER UPDATE CONTENTS
t
Annual User Recertification Requirements
CEW Warnings
CEW Targeting/Tactical Considerations
CEW Smart Use Considerations
CEW Medical Overview
1
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: © 2018 Axon Enterprise, Inc.

## Slide 3: ANNUAL RECERTIFICATION REQUIREMENTS
Review this PowerPoint
Receive and review current version of:
TASER Law Enforcement Product Warnings
CEW Study Aid: Smart Use Considerations
Pass Functional Test
Deploy a minimum of 2 live CEW cartridges into preferred target zones
2
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: It is highly recommended that any CEW user initially certified before May 2010 (Version 17) take and pass the current written user certification test at least once thereafter.
Instructors should incorporate pertinent information from TASER Training Bulletins issued after the release of this User Update.
If voluntary exposures are conducted during recertification training, be sure the proper Release form is signed and maintained.
© 2018 Axon Enterprise, Inc.

## Slide 4: TASER CEWS HAVE RISKS
At this time distribute, review and understand the current TASER product warnings
3
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: TASER Law Enforcement Product Warnings are contained in the instructor manual, the training DVD, and at https://www.axon.com/training/resources.
As required by TASER instructor training, you must check the Axon website within 72 hours of conducting this recertification training to ensure use of the most current warnings.
© 2018 Axon Enterprise, Inc.

## Slide 5: CEW ADVANTAGES
Most studied and most effective minimal force option
Reduces risk of injury to officers and suspects alike
Saves lives and de-escalates use of deadly force
Allows incapacitation from a distance
In probe mode, doesn’t rely on pain compliance
Displaying red LASER dot or arcing the current often achieves compliance without deployment
4
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: TASER CEWs have been the subject of more than 700 published studies, peer-reviewed papers, abstracts, and reports from numerous countries. A comprehensive CEW Research Index is available at https://www.axon.com/training/resources.
The DOJ National Institute of Justice 5-year Study of Deaths Following Electro Muscular Disruption (2011) (available at www.ncjrs.gov/pdffiles1/nij/233432.pdf) found that TASER CEW deployment “has a margin of safety as great or greater than most alternatives,” and carries a “significantly lower risk of injury than physical force.”
A PERF study (2010) found agencies using CEWs decreased suspect injuries requiring medical attention by 45% and decreased officer injuries requiring medical attention by 80%.
Courts have recognized “the important role controlled electric devices like the Taser X26 can play in law enforcement. The ability to defuse a dangerous situation from a distance can obviate the need for more severe, or even deadly, force and thus can help protect police officers, bystanders, and suspects alike.” Bryan v. MacPherson, 630 F.3d 805, 826 (9th Cir. 2010).
© 2018 Axon Enterprise, Inc.

## Slide 6: TACTICAL CONSIDERATIONS
Probe Placement Considerations
Limited CEW Effectiveness
Other Tactical Considerations
5
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: © 2018 Axon Enterprise, Inc.

## Slide 7: TARGETING
Avoid intentionally targeting the CEW on sensitive areas of the body such as the head, throat, breast/chest or area of the heart, genitals, or known pre-existing injury areas without legal justification
6
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: © 2018 Axon Enterprise, Inc.

## Slide 8: PREFERRED TARGET ZONE REAR
Below neck (blue zone)
(when practical)
The back is always the preferred target area when reasonably practical
Larger muscles
Clothing fits tighter
Surprise factor
Decreases risk of probe strike to eyes, throat, chest/breasts or genitals
7
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: © 2018 Axon Enterprise, Inc.

## Slide 9: PREFERRED TARGET ZONE FRONT
Lower torso (blue zone below chest)
(when practical)
More effective
- Larger muscles
Reduces the risk of hitting sensitive body areas
Increases dart-to-heart safety margin distance
Do not intentionally target genitals
8
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: Target Zone:
There have been some ineffective hits to the upper torso with narrow probe spreads where incapacitation was not achieved and subjects ripped out the probes. By lowering the point of aim to the lower torso on the front of the body, the potential for neuro-muscular incapacitation of the core muscles is increased. Safety is also increased since aiming for the lower torso reduces the risk of hitting some sensitive body areas, including the chest.
Dart-to-Heart Distance:
Experts have identified a close heart-to-dart distance as being the key determining factor in whether a CEW can deliver sufficient electrical charge to electrically affect the heart. The further a CEW dart is away from the heart, the lower the risk of cardiac arrest.
© 2018 Axon Enterprise, Inc.

## Slide 10: NEURO-MUSCULAR INCAPACITATION (NMI)
CEWs may not achieve total NMI
NMI levels range from limited area effects to significant body lockup
The greater probe spread, the higher likelihood of NMI
Subject may maintain muscle control, particularly in arms and legs
Be prepared with other force options, including a drive (or touch) stun follow up away from the probes to expand NMI area
Drive (or touch) stuns alone cause localized pain, not NMI
9
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: Even with both probes making contact in a preferred target zone with a large spread, a subject may be able to voluntarily move his arms and legs. The subject might be able to access and manipulate a weapon or strike/kick at an approaching officer. When reasonably safe and practicable, officers should attempt to gain physical control of subjects as quickly as possible to restrict their movement and minimize any threats.
© 2018 Axon Enterprise, Inc.

## Slide 11: PROBE SPREAD
Greater probe spreads generally increase effectiveness
12”+ spread optimal
Deployment distance 7-15 feet (2-4.5 meters)
Probe spreads under 4” typically create pain effect only
Exception is close probe spreads where one probe is above the waist and one is below the waist causing loss of balance and ability to stand
Consider deploying a second cartridge or using a 3-point drive stun if spread is insufficient to cause NMI
10
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: Deployments from 7 to 15 feet are within the preferred CEW range. There is a higher probability the probes will impact the subject, a good probe spread is generally achieved, and there is typically enough muscle affected to cause NMI. The officer is also a relatively safe distance from the subject and has time to react.
Remember, the bottom probe is traveling at a downward angle relative to the position of the CEW. Line up the TASER CEW with the subject’s body to get both probes on target.
© 2018 Axon Enterprise, Inc.

## Slide 12: SPLIT THE BELTLINE
For close-range deployments from 0-7 feet (0-2 meters):
Target the waist area to “split the belt line”
- Affects core muscles
needed for balance
- Increases officer and
cardiac safety
Avoid the genitals when practical
11
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: At ranges shorter than 7 feet, there is an increased probability that you can get both probes on target, but there will be very little probe spread or NMI. Close probe spreads in the chest area often do not achieve NMI and subjects can still control their arms, pulling out probes or breaking wires. We have seen impressive results with aiming near the waistline and placing one probe above the beltline and the other probe below the beltline. Particularly when firing at close range, place one probe into the thigh, leg or buttocks for enhanced effectiveness. This technique increases the chances of achieving at least partial NMI with a limited probe spread.
© 2018 Axon Enterprise, Inc.

## Slide 13: SOME CAUSES OF LIMITED CEW EFFECTIVENESS
Miss or single dart hit
Incomplete, broken, or intermittent circuit
Loose or thick clothing
Low nerve or muscle mass hit
Obese subject
Limited probe spread
Wires break
Operator error
12
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: © 2018 Axon Enterprise, Inc.

## Slide 14: LOOK FOR CHANGES IN BEHAVIOR
Look AND listen when evaluating the effectiveness of a CEW deployment
Watch the subject’s reaction and look for a change in behavior
Loud arcing sound typically indicates no or intermittent connection
Intermittent arcing typically indicates a poor connection such as a clothing disconnect
13
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: © 2018 Axon Enterprise, Inc.

## Slide 15: ARCING SOUNDS
If you hear a loud arcing noise and see no change in subject behavior, think bad connection
Reload (X26/X26P) and target different area or 3-point drive stun follow-up with cartridge still attached
For X2 deploy second cartridge
14
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: If the subject is not reacting and the electrical arc is loud during a field deployment, the electric charge is likely not being delivered. A quiet pulsing sound typically indicates a good connection. When no electrical charge is being delivered, the electricity will arc across the front electrodes of the CEW or across the electrodes on the front of a previously deployed cartridge, making a louder noise.
Use conductive practice targets in training to simulate the sound of a good field deployment. Axon offers a conductive full-size target for this purpose. The targets come in both upper and lower body and in front and back configurations showing the preferred target zones. Unlike previous targets, students can now aim for lower body and legs. This target gives auditory feedback for hits and misses consistent with what would be heard in actual deployments.
© 2018 Axon Enterprise, Inc.

## Slide 16: TACTICAL CONSIDERATIONS
Avoid TASER CEW over-dependence
Have reasonable and appropriate force options available
Consider cover and distance tactics
When practical:
Have at least one back-up officer present to control/cuff under power
Optimize choice of landing zone
Deploy to back (rather than front)
15
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: Although the advantages of using the TASER CEW have been proven in the field time and time again, it may not be the best answer to every problem you encounter, and it won’t always be effective. Consider having lethal cover or other reasonable and appropriate force options available when practical. Consider your cover and distance tactics when dealing with subjects who are reasonably perceived as an immediate threat.
© 2018 Axon Enterprise, Inc.

## Slide 17: TACTICAL CONTINGENCIES
CEW may have limited or no effect
No weapon system will operate or be effective all the time
A CEW or cartridge may not fire
Do not attempt to reuse a “dud” cartridge and carry a spare cartridge if possible per department policy
Be prepared to transition to other force options
16
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: TASER CEWs are sophisticated electronic devices that are subjected to the challenging law enforcement environment. Have contingency plans for dealing with ineffective deployments. If a CEW, cartridge, or accessory is inoperable or fails to function or achieve the desired effect, consider reloading and redeploying, using other force options, or disengaging. The failure of the CEW to fire, operate, or cause NMI could result in death or serious injury. See current TASER product warnings.
If a TASER cartridge is a dud, keep the CEW aimed at the target while shifting the safety switch to the down (SAFE) position as it may fire after a delay. If the CEW is aimed off target when the cartridge discharges, the probes could hit an unintended target.
© 2018 Axon Enterprise, Inc.

## Slide 18: BE CAREFUL OF DISTRACTIONS
Officers have been accused of using excessive CEW exposures due to stress or distractions, including nearby family members, bystanders, and incident witnesses
Distraction or situational stress may result in electrical discharge of unintended duration if the officer inadvertently holds the trigger down
Be alert to and avoid potential distractions that may result in extended exposures or unintentional additional applications
17
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: Know your trigger operation and battery type. The X26 CEW’s standard 5-second cycle, activated by pulling and releasing the trigger, can be cut short by engaging the safety or extended by holding the trigger back. Use of the Auto-Shut Down Performance Power Magazine (APPM) with X26P/X2 Smart Weapons allows the agency, at its discretion, to disable the continuous discharge feature and require a hard stop after 5 seconds.
© 2018 Axon Enterprise, Inc.

## Slide 19: CONTROLLING/CUFFING UNDER POWER
Use each 5-second CEW cycle as a “window of opportunity” to establish control/cuff while subject is affected
You can go hands on with the subject during the 5-second cycle without getting shocked
Do not place hands on or between probes
Do not touch wires
18
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: There is a natural reluctance to touch a person who is being shocked by electricity. But remember, you can grab onto a person during the 5-second cycle without feeling the effects of the discharge. You will not feel the electrical current unless you touch directly between or directly onto one of the probes. If this does happen, you will not be incapacitated. You will feel a shock and instinctively pull your hand away. Just reassess the subject and grab him somewhere else.
There have been incidents where subjects have been exposed to multiple CEW cycles because the subject would not comply with verbal surrender commands following a CEW deployment. Contact officers were available but did not move in during the cycle while the subject was incapacitated. Cuffing a subject under power may eliminate the need for additional exposures. Remember that each CEW 5-second cycle, deployment, or trigger pull must be legally justified.
© 2018 Axon Enterprise, Inc.

## Slide 20: TACTICAL CONSIDERATIONS
Be aware of the maximum range of your cartridges
Keep sufficient slack in the wires
Move with the subject if they start to roll
Failure to do so may result in wire breakage or probe disconnect causing loss of CEW contact with the subject
19
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: © 2018 Axon Enterprise, Inc.

## Slide 21: SMART USE CONSIDERATIONS
Hand out CEW Study Aid
20
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: This 1-page CEW Study Aid with Smart Use Considerations is located at https://www.axon.com/training/resources. These guidelines may be more conservative than Constitutional standards and do NOT establish any standard of care. They are intended to assist in forming the basis for reasonably safe and effective CEW use.
Optional (agency discretion):
Study Aid: Understanding the 4th Amendment's Objective Reasonableness Standard and Qualified Immunity.
IPICD Roll Call Mini-Poster™: Excited-Agitated Delirium and Sudden In-Custody Death, Excited Delirium (ED), Agitated Delirium (AD), Acute Behavioral Disorder.
© 2018 Axon Enterprise, Inc.

## Slide 22: SMART USE CONSIDERATIONS
When objectively reasonable and as practicable
If no exigency or immediate safety risk exists, slow down and consider alternative force options/solutions including negotiation, commands, or physical skills
Do not immediately resort to CEW
Physical resistance or mental illness alone does not indicate immediate threat
21
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: © 2018 Axon Enterprise, Inc.

## Slide 23: SMART USE CONSIDERATIONS
When objectively reasonable and as practicable
Choose a force option reasonably likely to cure the immediate safety risk
Use CEW only on those “actively resisting” or higher
Subject’s non-deadly danger to self does not justify higher risk of force
CEWs do not replace deadly-force options
22
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: © 2018 Axon Enterprise, Inc.

## Slide 24: SMART USE CONSIDERATIONS
Use CEW within:
Law
Department policy and training
Do not use CEW for:
Verbal defiance
Belligerence
Punishment
Horse play
23
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: © 2018 Axon Enterprise, Inc.

## Slide 25: SMART USE CONSIDERATIONS
When objectively reasonable and as practicable
Give verbal warning before CEW use
Give subjects a reasonable opportunity to comply before CEW is used or repeated
Consider if medical/mental condition is limiting compliance
Immediately cease any force once subject is under control
24
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: © 2018 Axon Enterprise, Inc.

## Slide 26: SMART USE CONSIDERATIONS
Avoid using CEW drive stuns except:
3 or 4-point contact to complete circuit or increase probe spread
“break-contact” or distraction tactic create reactionary distance
brief application to attempt pain compliance
Do not repeat drive stuns if compliance not achieved
Do not use drive stuns if pain is unlikely to gain compliance due to mind-body disconnect (psychotic episode) or increased pain tolerance (drugs/alcohol)
25
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: © 2018 Axon Enterprise, Inc.

## Slide 27: CEW MEDICAL/RISKS OVERVIEW
Higher risk populations
Injuries from falls
Increased injury risk examples
Flammability Risks
Cardiac Risks
Physiologic/Metabolic Effects
26
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: © 2018 Axon Enterprise, Inc.

## Slide 28: HIGHER RISK POPULATIONS
CEWs, like other force options, have not been laboratory tested on:
Pregnant women
Mentally ill
Elderly
Small children
Low body-mass (very thin) persons
CEW use on these individuals could increase the risk of death or serious injury
27
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: While a TASER CEW deployment may be appropriate to use on these subjects under the totality of the circumstances, always balance the risk of injury versus the risk of the threat.
© 2018 Axon Enterprise, Inc.

## Slide 29: INJURIES FROM FALLS
CEWs frequently cause subject to fall
Falls are often uncontrolled
Falls, even from ground level, can cause serious injuries or death (especially on hard surfaces)
Always consider environment subject is standing on
Consider if you would be justified in tackling or intentionally grounding
28
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: © 2018 Axon Enterprise, Inc.

## Slide 30: INCREASED INJURY RISK EXAMPLES
Elevated position
In water, mud/muck (drowning risk)
Operating machinery/vehicle
Running or in motion (bike/skateboard)
Sensitive target areas (head/eyes/groin)
Probes in heart or chest area
Repeated or continuous CEW discharges
29
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: © 2018 Axon Enterprise, Inc.

## Slide 31: FLAMMABILITY
TASER CEWs can ignite explosive materials, liquids, fumes, gases, vapors, and gels
Some personal defense sprays use flammable carriers such as alcohol and can be dangerous if used in immediate conjunction with CEWs
30
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: © 2018 Axon Enterprise, Inc.

## Slide 32: CARDIAC RISKS
Experts have identified the following key factors related to CEW cardiac risks:
Dart-to-heart distance
Duration of delivered electrical charge
The further the CEW dart is away from the heart and the fewer CEW cycles applied, the lower the risk of the CEW affecting the heart
31
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: © 2018 Axon Enterprise, Inc.

## Slide 33: CARDIAC RISKS
CEW cardiac risks are low, but not zero
To reduce cardiac risks (when possible):
Target the back
Avoid targeting the chest
Avoid prolonged or continuous exposures
32
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: © 2018 Axon Enterprise, Inc.

## Slide 34: PHYSIOLOGIC/ METABOLIC RISKS
CEWs may produce effects that could increase the risk of sudden death, including changes in:
Blood chemistry
Blood pressure
Respiration
Heart rate and rhythm
Adrenaline and stress hormones
The longer the CEW exposure, the greater the potential effects
33
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: © 2018 Axon Enterprise, Inc.

## Slide 35: AVOID REPEATED/EXTENDED CEW DURATIONS
Minimize the number and duration of CEW exposures
CEW exposure is a physically and psychologically stressful event
Use the shortest duration of CEW exposure objectively reasonable to accomplish lawful objectives
Avoid repeated or continuous exposures beyond 15 seconds absent reasonably perceived immediate threat and increased justification
Reassess the subject’s behavior before repeating or continuing the exposure, and provide time for compliance
34
© 2018 Axon Enterprise, Inc.
V.20.2 Update 01-15-18
Notes: Several law enforcement groups (e.g. IACP, PERF, COPS, DOJ) have established 15 seconds of CEW exposure (multiple applications or continuous) as a significant safety point. Be sure to discuss our own agency’s CEW policy.
© 2018 Axon Enterprise, Inc.

## Slide 36
THANK YOU!
Notes: © 2018 Axon Enterprise, Inc.